## Slide 1: Introduction
home automation communication protocol
it uses power line wiring for signaling and control
short radio frequency bursts hold the digital information

## Slide 2: Power line carrier control
the digital data is send on the electrical wiring of the household devices and light wiring
the data is encoded on a 120 kHz carrier frequence, transmitted as short bursts
data consists of an address and a command
data is sent from controller to the device
advanced devices can receive/request with a more advanced status
  status may be: on/off, dimming level, temperature or other sensing reading.

## Slide 3: Protocol
The transmitted X10 packages consists:
  4bit house code followed by 1-4bit unit codes followed by 4bit command
for more convinient system configuration:
  house code is selected as a letter from A - P
  unit code is a number from 1 - 16
each device is configured to respond to one of the 256 possible addressed (16 x 16)
the device reacts to commands specifically addressed to it, or to a broadcast
transmitted message example:
  "select A3" followed by "turn on", which means:
  unit "A3" should turn on its device
One-way devices: only receive commands and do not ACK their status
Two-way devices: ACK their status to the network. More expensive